## Slide 1: Key Derivation from Noisy Sources with More Errors than Entropy
Ran Canetti, Benjamin Fuller, Omer Paneth, Leonid Reyzin, and Adam Smith
Oct 22, 2014
(also Penn State, Tel Aviv University, MIT Lincoln Lab)
Notes: 1
1

## Slide 2: Key Derivation from Noisy Sources
Physically Unclonable Functions (PUFs)
Biometric Data
Goal of this talk: produce good outputs in scenarios we couldn’t handle before
High-entropy sources are often noisy
  Initial reading w0 ≠ later reading reading w1
  Assume a bound on distance: d(w0, w1) ≤ t
Goal: derive a stable cryptographically strong output
  Want w0, w1 to map to same output
  The output should look uniform to the adversary
Notes: http://sigma.octopart.com/14152599/image/Microchip-TC14433EPG.jpg
http://www.drgaelriverz.com/images/Round_Eye.JPG

## Slide 3: Fuzzy Extractors: Functionality [Wyner75] … [BennettBrassardRobert85] …lots of work… [DodisOstrovskyReyzinSmith04] …
Enrollment algorithm Gen: Take a measurement w0 from the source. Use it to “lock up” a random output in a nonsecret value p.
Subsequent algorithm Rep: give same output if d(w0, w1) < t
Security: r looks uniform even given p, whenever the source is good enough
w0
r
p
r
w1
< t
Gen
Rep

## Slide 4: Fuzzy Extractors: Goals
Goal 1: handle as many sources as possible (typically, any source in which w0 is 2k hard to guess)
Goal 2: handle as much error as possible (typically, any w1 within distance t)
Most previous approaches are analyzed in terms of t and k
w0
r
p
r
w1
< t
Gen
Rep
entropy k
This work: handle t > k

## Slide 5: Fuzzy Extractors: Typical Construction
Gen
Rep
w0
r
p
Ext
Ext
(converts high-entropy sources to uniform, e.g., via universal hashing)
w1
< t
r
entropy k
- correct errors using a secure sketch
- derive r using a randomness extractor
(gives recovery of the original from a noisy signal e.g., via the “checksum” bits of an error-correcting code)

## Slide 6: Fuzzy Extractors: Typical Construction
Gen
Rep
w0
r
p
Ext
Ext
w1
Sketch
Rec
w0
< t
r
entropy k
(converts high-entropy sources to uniform, e.g., via universal hashing)
- correct errors using a secure sketch
- derive r using a randomness extractor
(gives recovery of the original from a noisy signal e.g., via the “checksum” bits of an error-correcting code)

## Slide 7: Problem with Secure Sketches
Gen
Rep
w0
r
p
Ext
Ext
w1
p must store enough information to let you recover w0
How much information is that?
Sketch
Rec
w0
r
entropy k
< t

## Slide 8: Problem with Secure Sketches
Rep
w0
p
Ext
w1
p must store enough information to let you recover w0
How much information is that?
w0 could be anywhere within distance t, so log|Bt | > t bits
No security left if t > k (can be made rigorous for large classes of sources)
Our approach: give up on trying to recover w0
Rec
w0
< t
Bt
r
stores t bits about w0
has k < t bits of entropy
Notes: ADS: Is giving up on reconstruction really the contribution here?

## Slide 9: Is it possible to handle “more errors than entropy” (t > k)?
Consider some distribution for w0 with entropy k
Suppose t > k
Then |Bt| > 2k
Possibly |Bt| > # of possibilities for w0
Possibly all w0 lie in a single ball
No matter what we do, adversary can get the output by running Rep on w1 = center of that ball
No construction that is analyzed only in terms of t and k can be secure!
E.g., irises: log |Bt| ≈ 900 but k ≈ 250
w1
r
Rep
t
Notes: ADS: Bullet structure too simple here: these items don’t all belong in one list

## Slide 10: Is it possible to handle “more errors than entropy” (t > k)?
Consider some distribution for w0 with entropy k
Suppose t > k
Then |Bt| > 2k
Possibly |Bt| > # of possibilities for w0
Possibly all w0 lie in a single ball
No matter what we do, adversary can get the output by running Rep on w1 = center of that ball
No construction that is analyzed only in terms of t and k can be secure!
E.g., irises: log |Bt| ≈ 900 but k ≈ 250
But not all in a single ball!
w1
r
Rep
t
Moral: our constructions will exploit structure in the source (not “any source of a given k” like prior work)

## Slide 11: Idea: “encrypt” r using parts of w0
w0 = a1 a2 a3 a4 a5 a6 a7 a8 a9
Source: a string of symbols, arbitrary alphabet
Errors: Hamming
Gen: - get random combinations of symbols in w0
r
p
Gen
a3 a9 a5
r
r
a1 a9 a2
r
r
a3 a4 a5
r
r
a7 a5 a6
r
r
a2 a8 a7
r
r
a3 a5 a2
r
r
- “lock” r using these combinations
r

## Slide 12: Idea: “encrypt” r using parts of w0
w0 = a1 a2 a3 a4 a5 a6 a7 a8 a9
Source: a string of symbols, arbitrary alphabet
Errors: Hamming
Gen: - get random combinations of symbols in w0
r
p
Gen
a3 a9 a5
r
r
a1 a9 a2
r
r
a3 a4 a5
r
r
a7 a5 a6
r
r
a2 a8 a7
r
r
a3 a5 a2
r
r
- “lock” r using these combinations
r

## Slide 13: Idea: “encrypt” r using parts of w0
w0 = a1 a2 a3 a4 a5 a6 a7 a8 a9
Source: a string of symbols, arbitrary alphabet
Errors: Hamming
- “lock” r using these combinations
Gen: - get random combinations of symbols in w0
r
p
Gen
r
a3 a9 a5
r
r
a1 a9 a2
r
r
a3 a4 a5
r
r
a7 a5 a6
r
r
a2 a8 a7
r
r
a3 a5 a2
r
r

## Slide 14: Idea: “encrypt” r using parts of w0
w0 = a1 a2 a3 a4 a5 a6 a7 a8 a9
a1 a9 a2
r
a3 a9 a5
r
a3 a4 a5
r
a7 a5 a6
r
a2 a8 a7
r
a3 a5 a2
r
Source: a string of symbols, arbitrary alphabet
Errors: Hamming
- “lock” r using these combinations
- = locks + positions of symbols needed to unlock
Gen: - get random combinations of symbols in w0
r
p
r
Gen
p

## Slide 15: Idea: “encrypt” r using parts of w0
w0 = a1 a2 a3 a4 a5 a6 a7 a8 a9
a1 a9 a2
r
a3 a9 a5
r
a3 a4 a5
r
a7 a5 a6
r
a2 a8 a7
r
a3 a5 a2
r
Source: a string of symbols, arbitrary alphabet
Errors: Hamming
- “lock” r using these combinations
- = locks + positions of symbols needed to unlock
Gen: - get random combinations of symbols in w0
r
p
r
Gen
p

## Slide 16: Idea: “encrypt” r using parts of w0
a1 a9 a2
r
a3 a9 a5
r
a3 a4 a5
r
a7 a5 a6
r
a2 a8 a7
r
a3 a5 a2
r
Source: a string of symbols, arbitrary alphabet
Errors: Hamming
- “lock” r using these combinations
- = locks + positions of symbols needed to unlock
Gen: - get random combinations of symbols in w0
p
r
p

## Slide 17: Idea: “encrypt” r using parts of w0
a1 a9 a2
r
a3 a9 a5
r
a3 a4 a5
r
a7 a5 a6
r
a2 a8 a7
r
a3 a5 a2
r
Source: a string of symbols, arbitrary alphabet
Errors: Hamming
- “lock” r using these combinations
- = locks + positions of symbols needed to unlock
Gen: - get random combinations of symbols in w0
p
r
p
Rep:
w1 = a1 a2 a3 a4 a5 a6 a7 a8 a9
r
Rep

## Slide 18: Idea: “encrypt” r using parts of w0
a1 a9 a2
r
a3 a4 a5
r
a7 a5 a6
r
a2 a8 a7
r
a3 a5 a2
r
Source: a string of symbols, arbitrary alphabet
Errors: Hamming
- “lock” r using these combinations
- = locks + positions of symbols needed to unlock
Gen: - get random combinations of symbols in w0
p
r
p
w1 = a1 a2 a3 a4 a5 a6 a7 a8 a9
r
Rep
a3 a9 a5
r
Rep:

## Slide 19: Idea: “encrypt” r using parts of w0
a1 a9 a2
r
a3 a4 a5
r
a7 a5 a6
r
a2 a8 a7
r
a3 a5 a2
r
Source: a string of symbols, arbitrary alphabet
Errors: Hamming
- “lock” r using these combinations
- = locks + positions of symbols needed to unlock
Gen: - get random combinations of symbols in w0
p
r
p
w1 = a1 a2 a3 a4 a5 a6 a7 a8 a9
r
Rep
a3 a9 a5
r
Rep: Use the symbols of w1 to open at least one lock

## Slide 20: Idea: “encrypt” r using parts of w0
a1 a9 a2
r
a3 a4 a5
r
a7 a5 a6
r
a2 a8 a7
r
a3 a5 a2
r
Source: a string of symbols, arbitrary alphabet
Errors: Hamming
- “lock” r using these combinations
- = locks + positions of symbols needed to unlock
Gen: - get random combinations of symbols in w0
p
r
p
w1 = a1 a2 a3 a4 a5 a6 a7 a8 a9
r
Rep
Rep: Use the symbols of w1 to open at least one lock
a3 a9 a5
r
r

## Slide 21: Idea: “encrypt” r using parts of w0
a1 a9 a2
r
a3 a4 a5
r
a7 a5 a6
r
a2 a8 a7
r
a3 a5 a2
r
Source: a string of symbols, arbitrary alphabet
Errors: Hamming
- “lock” r using these combinations
- = locks + positions of symbols needed to unlock
Gen: - get random combinations of symbols in w0
r
p
Rep: Use the symbols of w1 to open at least one lock
a3 a9 a5
r
r
Error-tolerance: as long as at least one combination is ok
Security: each combination must have enough entropy
(sampling of symbols must preserve sufficient entropy)

## Slide 22: How to implement locks?
A lock is the following program:
  If input = a1 a9 a2, output r
  Else output 
a1 a9 a2
r
Obfuscate this program!
  Obfuscation: preserve functionality, hide the program
  Obfuscating this specific program gives a “digital locker”: encryption of r that is secure even multiple times with correlated and weak keys [Canetti Kalai Varia Wichs 10]
  For this specific program: obfuscation is practical (R.O. or DL-based) [Canetti Dakdouk 08], [Bitansky Canetti 10]
  For example (R.O. model): lock = r  H(a1 a9 a2)
  Hiding r as long as the input can’t be exhaustively searched (superlogarithmic entropy)
Notes: ADS: Say RO construction first? Then say point obfuscation?

## Slide 23: How to implement locks?
a1 a9 a2
r
Q: if you are going to use obfuscation, why bother? Why not just obfuscate the following program for p
  If distance between w0 and the input is less than t, output r
  Else output 
A: you can do that [Bitansky Canetti Kalai Paneth 14], except it’s very impractical + has a very strong assumption
A lock is the following program:
  If input = a1 a9 a2, output r
  Else output 

## Slide 24: How good is this construction?
We can correct more errors than entropy!
For correctness: t < constant fraction of symbols
Another construction for t = constant fraction for really large alphabets (in the paper)
a1 a9 a2
r
a3 a9 a5
r
a3 a4 a5
r
a7 a5 a6
r
a2 a8 a7
r
a3 a5 a2
r

## Slide 25: How good is this construction?
We can correct more errors than entropy!
For correctness: t < constant fraction of symbols
Another construction for t = constant fraction for really large alphabets (in the paper)
Note: computational, not information-theoretic, security (a different info-theoretic construction in the paper)
a1 a9 a2
r
a3 a9 a5
r
a3 a4 a5
r
a7 a5 a6
r
a2 a8 a7
r
a3 a5 a2
r
Notes: ADS: too much text (break it up somehow?)

## Slide 26: How good is this construction?
It is reusable!
  Same source can be enrolled multiple times with multiple independent services
w0
r
p
Gen
w0'
r'
p'
Gen
w0''
r''
p''
Gen
Secret even given
p, p', p'', r, r''

## Slide 27: How good is this construction?
It is reusable!
  Same source can be enrolled multiple times with multiple independent services
  Follows from composability of obfuscation
  In the past: difficult to achieve, because typically new enrollments leak fresh information
  Only previous construction [Boyen 2004]: all reading must differ by fixed constants (unrealistic)
  Our construction: each reading individually must satisfy our conditions

## Slide 28: Conclusion
It is possible to cover sources with more errors than entropy!
Exploit the source
Don’t aim for secure sketches (i.e., full error correction)
It is also possible to get reusability!
Use computational security
t

## Slide 29: Follow-up
if the adversary knows more about the source than you do
w1
r
Rep
t
Minimum necessary condition for fuzzy extraction: weight inside any Bt must be small
Let Hfuzz(W) = log (1/max wt(Bt))
Big Hfuzz(W) is necessary
Q: Is big Hfuzz(W) sufficient for fuzzy extractors?
A1: Yes if security is computational (using obfuscation) [Bitansky Canetti Kalai Paneth 14]
A2: No if security is information-theoretic
A3: No if you try to build a secure sketch
Notes: ADS: Emphasize “Yes, if FE designer knows a description of the distribution”

## Slide 30: Questions?